## Slide 1: 1b.3
D-band SiGe Subharmonic Downconverter with Dynamic Conversion Gain and Fixed Input Compression
Jonathan Tao, James Buckwalter
University of California, Santa Barbara
UC Santa Barbara Santa Barbara, California 93106

## Slide 2: Motivation
Power consumption above 100 GHz is prohibitive:
  mobile applications
  Radar-radio fusion on platform
LO system power dominates receiver power consumption
Reduce power in LO chain dynamically with channel conditions

## Slide 3: Goals of This Work
X4 Subharmonic downconverter at D-band (110 GHz – 170 GHz)
Linearize gain on LO frequency multiplier
  backoff controllability to save power
Simplify circuit to save power and to integrate into an array

## Slide 4: Problem: Gain Sensitivity
Typical multiplier chains operate at a single saturating power
High gain sensitivity in back-off power conditions: poor controllability
Simulation on frequency doubler with different biases for optimization

## Slide 5: Push-pull Frequency Multipliers
Conventional Multiplier
Input is rectified to produce pulsed waveform
We can get a 4th harmonic
But there is an additional DC current
  Affects biasing and gain
  Causes extreme gain sensitivity to power
Fourier Series

## Slide 6: Proposed Downconverter
Active Load
Mixer
X4 Frequency
Multiplier

## Slide 7: Feedback Bias Analysis
Equivalent DC Model

## Slide 8: Proposed Design: Feedback Bias
Parallel transistors shorted at DC: treat as one
Simplifying assumptions:
Feedback Bias has stable bias point:
Current change suppressed by negative feedback on VBE
Equivalent DC Model

## Slide 9: Simulated Effect of Static Biasing
With -6 dB LO backoff from peak gain
  17 dB more gain than static biased version
Obtain higher performance at back-off and less sensitive gain

## Slide 10: Layout
Global Foundries 9HP+
  90-nm SiGe BiCMOS
Core: 0.56 mm x 0.35 mm

## Slide 11: Measurement
Results calibrated with reference power meter (scalar measurement)
Differential mismatch compensated with time delay in oscilloscope

## Slide 12: Conversion Gain Over Frequency
Reliable control of conversion gain over a wide LO power range
LO port frequency shift led to better match at target LO frequency

## Slide 13: Power Consumption Tradeoff
Back off LO power from -5 dBm to -11 dBm
  Trade 11.7 dB of gain to save 35% power
155 GHz RF with 140 GHz LO

## Slide 14: Compression and Power Detector
Input compression is insensitive to LO power variation
Feedback bias circuit can be used for LO power detection

## Slide 15: Conclusion
A fourth subharmonic D-band downconverter is implemented with bias feedback
  Demonstrates reliable LO power backoff to save power
Achieves a high multiplication factor without sacrificing additional area, power consumption, or LO power requirement

## Slide 16: Acknowledgements
This work was supported by the Semiconductor Research Corporation (SRC) under the JUMP program, Cognisense
The authors appreciate the support of GlobalFoundries for access to the 9HP+ process.

## Slide 17: Comparison References
[3] A. Moradinia, Y. A. Mensah, B. L. Ringel, and J. D. Cressler, “A 117–155-GHz SiGe HBT D-Band Subharmonic Mixer Utilizing a Novel 180° Hybrid Coupler,” IEEE Microwave and Wireless Technology Letters, vol. 33, no. 6, pp. 731–734
[6] K. Schmalz, W. Winkler, J. Borngr¨aber, W. Debski, B. Heinemann, and J. C. Scheytt, “A Subharmonic Receiver in SiGe Technology for 122 GHz Sensor Applications,” IEEE Journal of Solid-State Circuits, vol. 45, no. 9, pp. 1644–1656,
[7] T. Maiwald, J. Potschka, K. Kolb, M. Dietz, A. Hagelauer, A. Visweswaran, and R.Weigel, “A Broadband Zero-IF Down-Conversion Mixer in 130 nm SiGe BiCMOS for Beyond 5G Communication Systems in D-Band,” IEEE Transactions on Circuits and Systems II: Express Briefs, vol. 68, no. 7, pp. 2277–2281